GENERAL SAFETY INSTRUCTIONS

1.	No horse play is allowed: running, pushing, wrestling, throwing objects, ect.

2.    	Obtain permission from the instructor each time you need to use a piece of power equipment.  You must pass the appropriate safety test.

3.    	No one, other than the one person using the machine and the instructor, may be inside the safety zone during machine operation.

4.    	Eye safety protectors must be worn in the shop at all times.

5.    	Long hair must be securely fastened back during use of machinery to avoid getting your hair caught in the moving parts.

6.    	No jewelry may be worn in the shop: rings, necklaces, watches, wristbands, ear rings, etc.

7.    	Keep your immediate work area clean at all times.

8.  	Wipe up spilled liquids immediately.

9.   	Loose clothing such as ties, torn clothing or similar garments which can become entangled in moving machinery shall not be worn where an entanglement might occur.  Tuck in shirt tails, roll up long sleeves, and tie aprons in the back.

10.  	Report all accidents, no matter how minor, immediately to the instructor.

11.   	Obtain permission from instructor before using flammable materials.

12.   	Place oily rags in the designated oily waste container.  Never put them in lockers or stack them in corners.

13.   	Do not touch the gas bottles without the instructor’s permission.

14.  	Report any equipment malfunctions to the instructor.

15.  	Notify the instructor in case you get shocked.

16.  	Do not use electrical equipment near moisture.

17.  	Do not stand on stools, chairs, benches, or other unstable objects.

18.  	Lift with your legs not your back.

19.   	Do not lift heavy objects above your shoulders.

20. 	Remind those around you of safe working practices if they are unsafe, then notify the instructor.

21.  	Never touch or talk to anyone using a power tool.

22. 	Never use a file that does not have a handle.

23. 	Never carry sharp tools in your pocket such as a chisel, cutting knife, screw driver, ect.

24. 	Never use a hammer with a loose head.

25. 	If the handles in the hammers, saws, chisels, etc., are cracked or broken, do not use them.  Report the damage to the instructor.

26.  	While doing work, be considerate of other people.  Be watchful with tools and never do something that might injure you or others.

27.  	All machines should be turned off when not in use.

28.  	When setting a plane down, lay it on it's side.

29. 	Do not watch other people while they are using the power tools.

30. 	Do not hold work for other students; it should be clamped or put in a vise.

31. 	Never place your hand in front of a screw driver or chisel, they could slip and cut you.

32.	Keep your hands away from moving parts.

33.	When working with hand tools or lights, wear work gloves.

BAND SAW SAFETY INSTRUCTIONS

1.  	Plan sawing procedure so you back out of the shortest cut.

2.    	Stop the machine if you hear unusual sounds. Then notify the instructor.

3.    	Cut only stock which has a flat surface which can rested on the band saw table.

4.	Cylindrical stock must be cut using a "v" block or a miter gage so that it does not spin out of your hands.

5.    	Check to see that all guards are in place.

6.    	Set upper saw guide 1/4 inch or a finger thickness above the stock to be cut.  Check with the instructor if stock is rough or warped.

7.	The saw blade must be stopped when making adjustments.

8.    	Ask your instructor to approve all special set ups.

9.    	Wear safety glasses or goggles at all times.

10.    	Hold material firmly or securely.

11.     	Keep fingers and hands out of the direct line of the saw blade.

12.   	Keep fingers a safe distance from the saw blade, no closer than 2 inches.  The edge of the insert plate is only one inch away.

13.	Feed material into machine at a moderate rate of speed, especially when cutting curves.

14. 	Allow the machine to come to a dead stop before backing the saw blade out of the cut.

15.  	Keep waste material from accumulating on the band saw table.  Allow the saw to come to a dead stop before removing waste material.

16.   	If the saw blade breaks or comes off:

a. Step away immediately.

b. Turn off power if it is possible to do so without endangering yourself.

c. Notify your instructor.

17.	Never stand to the side of the band saw.  A serious injury might result if a blade breaks.

18. 	The only adjustment a student may make is the upper band saw guide height.

19.  	When cutting long stock you must have the instructors help.

20.  	Use relief cuts when sawing tight curves.

SAFETY INSTRUCTIONS FOR THE DRILL PRESS

1.   	The work piece must be clamped in the vise or fastened to the table if the work piece is small, you are drilling large holes, or you are drilling metal.  If the drill bit catches and grabs the work from your hand, a severe injury may result.

2.    	Remove chips and shavings with a brush or piece of wood, never with your hands or a rag.

3.    	Keep your fingers away from the drill bit when the drill press is on.

4.    	Keep hair, fingers, jewelry, and loose clothing away from all moving parts of the drill press.

5.    	Check the machine to see that the chuck key, tools, and other accessories are removed from the table before turning the power on.

6.    	Use saw dust to clean up oil on or around the drill press.

7.    	When using a vise, operate the drill press in such a way that the drill will not damage the vise or table.

8.    	Use drill bits which are properly sharpened and which are the correct size.

9.    	When the drill bit begins to break through the material, ease up on the feed pressure so that the drill bit won't grab the work piece.

10.  	The drill press has a safety zone marked off on the floor with black and yellow striped tape.  No one, other than the one person using the drill press and the instructor, may be inside the safety zone during drilling operation.

11.  	If possible, secure the material in such a way that any overhang of the table is on the operator's left side.

12.  	Always use a  backing board on the drill press table to avoid damage to the table.

13.	use only sufficient feed pressure to allow the drill to cut evenly into the material.

14.	Do not stop the drill press by using your hand.

15.	If the work is seized or starts to spin:

a. Step away immediately.

b. Turn off power if it is possible to do so without endangering yourself.

c. Notify your instructor.

ROUTER

1.	Make sure the locking wing nut is tight so that the depth of cut will not change while you are using it.

2.	The collet nut should be tightened securely to prevent the router bit from slipping.

3.	When using a hand held router, hold onto the router while you turn it on.

4.	The router should be moved or the work fed into the cutter in such a way that the sharp edge of the cutter rotates into the work piece.  Follow the arrow if one is provided.

5.	The end grain should be routed first.

6.	The material must be clamped or held securely when using a hand held router.

7.	Feed the work piece or router just fast enough for the cutter to cut and not burn.

8.	Make several shallow cuts with the router removing only a small amount of material each time.  Removing a lot of material in one pass is unsafe and can cause damage to the wood.

9.	If the router bit does not have a pilot or bearing always use a fence.

10.	Turn off the router after you are through with your cuts.  Unplug hand held routers after the router bit has stopped.

11.	If you are using the router by hand, do not set the router where it can cause injury to a student or damage a workbench.

12.	Hold material firmly and approach the pilot or bearing slowly with the board.

13.	Students may not adjust the router or router fence.

14.	Never put your hand or fingers in line with the cutter.

15.	Never allow your hand or fingers to pass over the cutter even if covered by the work piece.

16.	Use a push stick when routing narrow or small stock.

ELECTRIC SANDERS

1.	Keep both hands on the handles of the belt sander.  This makes it impossible to feel the sanded surface while sanding, which would endanger your hand.

2.	Arrange the electric cord of the sander so that it cannot be caught by the abrasive paper.

3.	Hold on to the handle of the sander when you plug it into the electrical outlet.  This prevents possible damage to the machine. Someone might have left the switch on with out your knowledge. The machine could fall off the bench.

4.	Make certain that you select the correct size of belt or sheet and the proper grit of sand paper to do the job.

5.	Unplug the portable sander from the outlet when changing abrasive belts or sheets.

6.	Un plug the portable sander when you are not using the it and lay it on its side.

7.	If the belt on the stationary belt sander is not tracking properly (properly aligned with the wheels) immediately turn it off and tell the instructor. Do not try and fix it your self.

8.	Always lift a portable sander before starting to sand and also before turning off the power.

9.	The weight of the sander is sufficient to do normal sanding.  Do not 	exert more pressure. It will strain the motor.

10.	Turn off the power and do not put the sander down until it comes to 	a complete stop.

11.	Fasten the board or project securely.

12.  	Set the sander down evenly on the project or piece.  Move it back and forth at a moderate to slow rate.

DISC/BELT SANDER SAFETY INSTRUCTIONS

1.  	Check sanding belt or disc for breaks or tears.

2.  	Keep fingers away from abrasive surfaces of sanders; never attempt to stop the sander with your hands.

3.    	Sand against the rotation of the belt and on the down side of a disc sander.

4.    	Hold work securely.

5.    	Machine sand only objects large enough to hold safely against the sander.

6.    	Check with the instructor before sanding irregular or smaller objects.

7.    	Work piece must be large enough that it will not fit between the abrasive paper and the work table of the disc/belt sander.

8.    	Keep work moving evenly and steadily over the abrasive surface of the sander.

9.    	Apply only sufficient pressure to smooth surface being sanded on the disc/belt sander.

10.  	Turn off the disc/belt sander after use.

11.  	Do not make any adjustments on the sanders.

12.  	The disc/belt sander is for sanding edges only. Do not attempt to bevel the edges.